Building a custom Risc-V
open source FPGA SOC

---
Introduction
- Risc-V
- System on a Chip
- Open source hardware
- Open source tools
- VexRiscv, SaxonSoc and Blackice Mx

---
Risc-V
- Open source Instruction Set Architecture (ISA)
- Full-featured mature ISA
- Supported by Linux
- Supported by real-time Operating Systems
  - e.g. Zephyr
- Increasing industry support
- GCC and other tools support
- Rival to ARM

---
System-on-a-Chip (SOC)
- CPU plus peripherals on one chip
- There is one in your phone
- There is one in a Raspberry Pi
- Microcontrollers are simple SOCs

---
Risc-V implementations
- Sifive
- Picorv32
- Icicle
- VexRiscv
- Lots of others
  - see https://github.com/riscv/riscv-cores-list

---
Why build a custom FPGA SOC
- Open source all the way down
- Exactly those peripherals that you want
- As many of each peripheral as you want
- Hardware implementations - no bit-banging
- Simpler software device drivers
- Much faster peripherals like LED panels
- Complete control

---
My choices
- VexRiscv
- SaxonSoc
- Blackice Mx board

---
Why VexRiscv
- Fastest 32-bit FPGA implementation
- Most configurable implementation
- Full featured, e.g. supervisor mode and MMU
- Will run Linux
- Written in SpinalHDL

---
Why Blackice Mx
- Open source Ice40 board with SDRAM
- Scalable and modular with carrier boards
- Compatible with Linux-capable BlackEdge
- HDMI support
- Lots of I/O
- .. but also runs on many other boards
  - like TinyFPGA BX, iCEBreaker, Fomu, etc.

---
Why SaxonSoc
- Same author as VexRiscv (Charles Papon)
- Written in SpinalHDL
- Supports many peripherals and memory types
- Will run Linux
- Banana Memory Bus and APB3 peripheral bus
- Concise description of custom SOCs
- Generation of BSPs
- Experience from Murax and Briey SOCs
- SaxonSoc is currently experimental

---
SpinalHDL
- Uses Scala language
  - designed to support Domain Specific Languages
- Runs in Java VM
- Much nicer semantics than Verilog
- Much less error-prone than Verilog
- Real software-engineering tool
- Rivals: Chisel and Python Migen with Litex

---
Installation on Linux
- Install Icestorm
- Install dfu & latest firmware for Blackice board
- Install SpinalTemplateSbt
- Install SaxonSoc Bmb branch
- Build SOC with make file
- Can also use IDEs
  - e.g. IntelliJ and Visual Studio

---
Open Source toolchain
- SpinalHDL generates Verilog
- Yosys synthesises netlist
- Nextpnr place and route for specific FPGA chip
- Icepack produces ice40 bitstream

---
SaxonSoc code extract
  //Add components
  val ramA = BmbOnChipRamGenerator(0x80000000l)
  val uartA = Apb3UartGenerator(0x10000)
  val gpioA = Apb3GpioGenerator(0x00000)
  val spiA = Apb3SpiMasterGenerator(0x20000)
  val spiB = Apb3SpiMasterGenerator(0x30000)
  // Configure components
  ramA.size.load(8 KiB)
  ramA.hexInit.load("software/standalone/readSdcard/build/readSdcard.hex")
  uartA.parameter load UartCtrlMemoryMappedConfig(
    baudrate = 115200,
    txFifoDepth = 32,
    rxFifoDepth = 32
  )
  spiA.parameter load SpiMasterCtrlMemoryMappedConfig(
    SpiMasterCtrlGenerics(
      dataWidth = 8,
      timerWidth = 32,
      ssWidth = 1
    )
  )

---
SaxonSoc variants for Blackice Mx
- BlackiceMxSocMinimal - blinkAndEcho
- BlackiceMxSocSdram - writeFlash utility
- BlackiceMxXip - blinkAndEcho from flash
- BlackiceMxZephyr - runs Zephyr OS
- BlackiceMxArduino - supports Arduino IDE
  - based on f32c/arduino
- Produce your own

---
Demo of Zephyr OS
Philosophers sample

---
Questions
?